## Slide 1
BMU VERIFICATION PROJECT
From specification to bug evidence
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
01
A 32-bit BMU.
A complete verification story.
SystemVerilog + UVM
Directed + random testing
Assertions + coverage
17
operation classes
562
functional bins hit
9
open DUT findings
Original RTL. Reproducible failures.
Follow one MAX request from sequence creation to root-cause evidence.
Notes: Open with the verification objective: establish expected behavior and expose defects reproducibly. This is a training verification submission, not a claim of correct RTL. Ask the audience to remember one question: how do we know an output is right?
Evidence / source files:
README.md; docs/08_signoff/BMU_Signoff_Report.md
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 2
INTERACTIVE AGENDA
The route through the project
Click a section to jump there. Use MENU on any slide to return.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
02
01 Understand
Specification, controls, timing, DUT
02 Follow a request
Environment and MAX transaction
03 Test the design
Directed, random, assertions
04 Measure + debug
Coverage, results, nine findings
05 Correct + close
Existing fix code and validation gate
06 Explore details
Operations, evidence, commands
Audience checkpoints: predict a result • classify a failure • interpret coverage.
Notes: Allow roughly 25–30 minutes for the main story. Use the appendix for detailed questions. The cards are internal PowerPoint hyperlinks, active in Slide Show mode.
Evidence / source files:
README.md; presentation navigation
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 3
01 / UNDERSTAND
What does this BMU do?
32-bit operands in; a registered result and a live error out.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
03
Logic and shift
OR, XOR, SRL, SRA, ROR, BINV
Arithmetic and compare
SH2ADD, SUB, SLT/SLTU, signed MAX
Count and rearrange
CTZ, CPOP, SEXT.B, PACK, GREV
CSR data paths
Bypass read and write-data selection
Predict: CPOP(0xFFFF0000) = ? Keep your answer for the bug review.
Notes: Introduce the design without listing every mnemonic verbally. There are 17 operation classes; SLT and SLTU share one class. CSR write means selecting write data, not storing a CSR. Ask: what should CPOP of FFFF0000 return? Answer 16; revisit this in the bug discussion.
Evidence / source files:
README.md §2; docs/00_spec/BMU_Specification_v1.2.pdf
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 4
01 / UNDERSTAND
Turn the specification into checks
Example requirement: signed MAX selects the larger operand and requires SUB.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
04
REQUIREMENT
Signed MAX
max=1, sub=1
STIMULUS
a=10, b=20
valid_in=1
ORACLE
result=20
error=0
EVIDENCE
Compare + log
cover scenario
Negative companion test
Remove SUB: require error=1 and captured result=0.
Record ambiguities
Timing, GREV invalid encoding, CSR conflicts.
One selected operation can require several control bits. “Legal” is not simply one-hot.
Notes: Read requirements before writing stimulus. For MAX, distinguish data semantics from legal controls. Missing SUB should produce error=1 and captured result=0. Timing assumptions are documented separately. Traceability connects the requirement to a test, oracle, coverage target, and evidence.
Evidence / source files:
docs/02_test_plan/traceability_matrix.md; docs/03_clarifications_log/spec_clarifications_log.md; tb/packages/bmu_types_package.sv
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 5
01 / UNDERSTAND
The interface contract determines sampling
No ready signal. No output-valid handshake. valid_in enables result capture.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
05
Inputs
a_in, b_in: 32 bits
ap: 42 control bits
CSR enable + read data
rst_l, valid_in, scan_mode
Falling edge
Driver applies request
Between edges
Combinational paths settle
Rising edge
Capture result; monitor samples
valid_in=0 → result holds. Invalid controls can still assert the live error output.
Notes: Clock period is 10 ns. The driver changes the request at a falling edge. The monitor uses rising-edge input #0 sampling after nonblocking updates, pairing the observed request with its captured output. Reset clears result synchronously; error is live and suppressed during reset. These timing choices follow CLARIF-001.
Evidence / source files:
tb/interface/bmu_interface.sv; tb/top/bmu_tb_top.sv; tb/sequences/reset_ops/latency_check_seq.sv
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 6
01 / UNDERSTAND
Inside the DUT
Parallel datapaths feed a combined result; implemented error logic gates capture data.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
06
Inputs
a, b, ap
CSR signals
Logic / CSR read
Adder / compare
Shift / rotate
Count / pack / bits
Combine
Masked OR
error → zero
Result register
result_ff[31:0]
reset / enable / hold
Live error: implemented guards are incomplete
Data bugs and missing control guards need different checks.
Notes: This is an abstraction of the original RTL. The design combines masked path outputs with bitwise OR, then forces result data to zero on error. The error decoder implements only some required guards. Broader branch/prediction internals are outside the project functional scope. Clock/reset/enable control the final register.
Evidence / source files:
rtl/Bit_Manipulation_Unit.sv; rtl/rtl_param.sv
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 7
02 / FOLLOW A REQUEST
The UVM environment: two flows, one verdict
Stimulus travels toward the DUT. Observations fan out to checking and coverage.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
07
Sequence
Sequencer
Driver
Interface
DUT
Monitor
Reference model
Scoreboard + checker
expected
actual
Coverage
Scenarios exercised
Assertions
DUT outputs to interface
Active agent:
sequencer, driver, monitor
Predict from observed inputs. Compare both result_ff and error.
Notes: Point out the active agent: sequencer, driver, monitor. The sequence is a transaction producer. The virtual interface bridges classes to static signals. The monitor publishes the same observed transaction to the predictor, actual scoreboard input, and coverage. Predictor output connects to expected scoreboard input. Assertions observe interface signals independently.
Evidence / source files:
tb/env/bmu_environment.sv; tb/env/agents/bmu_agent/bmu_agent.sv; tb/top/bmu_tb_top.sv
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 8
02 / FOLLOW A REQUEST • STEP 1
Your turn: construct a legal MAX request
Before revealing the DUT output, predict what should happen.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
08
// Transaction values
rst_l = 1;
valid_in = 1;
ap.max = 1;
ap.sub = 1;
a_in = 10;
b_in = 20;
Question 1
Is max=1 alone a legal request?
Question 2
What are result_ff and error?
Think first. The next two slides reveal when the request is driven and what happens.
Notes: Ask the audience to choose the expected result and error. The legal control pair is max=1, sub=1. Every unlisted control is zero, CSR read is disabled, scan mode is zero, reset is high. bmu_sequence_item stores randomized request fields and nonrandom observed outputs. Click Continue to move to signal timing.
Evidence / source files:
tb/env/agents/bmu_agent/bmu_sequence_item.sv; tb/sequences/smoke/bmu_bug_seq.sv; results/bugs/BMU-BUG-010.txt
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 9
02 / FOLLOW A REQUEST • STEP 2
The request becomes pin-level activity
Sequence → sequencer → driver → interface → DUT
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
09
// UVM handshake — simplified
start_item(req);
// fill request fields
finish_item(req);
// Driver: get → drive → item_done
10 ns: falling edge
Drive MAX, SUB, a=10, b=20
10–15 ns: compute
Result path and live error settle
15 ns: rising edge
Register updates; monitor samples
Driver completion means the item was driven.
The scoreboard determines correctness.
Expected after capture: result_ff=20, error=0. The next slide reveals the actual result.
Notes: The code is a teaching sketch of the UVM handshake, not copied implementation. start_item/finish_item submit the transaction. The driver gets the next item, drives through cb_drv, then acknowledges it. The captured mismatch in the isolated MAX test is at 15 ns. Avoid suggesting item_done means DUT data correctness.
Evidence / source files:
tb/env/agents/bmu_agent/driver/bmu_driver.sv; tb/interface/bmu_interface.sv; results/bugs/BMU-BUG-010.txt
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 10
02 / FOLLOW A REQUEST • STEP 3
The scoreboard exposes the MAX defect
Same observed request. Independent prediction. Different data.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
10
EXPECTED
result_ff = 20
error = 0
ACTUAL
result_ff = 10
error = 0
VERDICT
Mismatch
BMU-BUG-010
@ 15 ns expected: 0x00000014 / error=0 actual: 0x0000000a / error=0
A scenario can be covered and incorrect at the same time.
Notes: Reveal the actual result 10. The reference model predicts signed max 20 from observed inputs and legal controls. Both error outputs are zero, so a guard assertion alone would not catch this data-selection defect. The coverage bin still gets hit. At 15 ns, the retained log records the mismatch. Two total comparisons include the reset sample.
Evidence / source files:
results/bugs/BMU-BUG-010.txt; tb/env/reference_model/bmu_reference_model.sv; tb/env/scoreboard/bmu_scoreboard.sv
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 11
02 / TRUST THE ENVIRONMENT
Who checks the checker?
A useful failure must distinguish a DUT defect from a testbench mistake.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
11
865 predictor self-checks
Legal, invalid, boundary and state cases
Passing setup checks
OR smoke and timing/reset tests
Complete comparisons
Result + error; four-state equality; queue checks
Honest failure detection
UVM errors, assertions and incomplete runs fail
Prediction is independent of RTL. Coverage shares specification classification helpers.
Notes: 865 predictor self-checks pass. They include legal cases, forbidden controls, modes, count boundaries, and reset/hold state. The predictor is independent from RTL datapaths, but classification helpers are shared with functional coverage. Four-state equality exposes X/Z differences; it is not a blanket proof of unknown rejection. Scoreboard checks no stimulus and unmatched queues. Timing tests protect sampling alignment.
Evidence / source files:
tb/tests/bmu_model_self_test.sv; tb/env/scoreboard/bmu_checker.sv; tb/env/scoreboard/bmu_scoreboard.sv; results/reports/regression_summary.csv
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 12
03 / CHALLENGE THE DESIGN
Directed testing asks precise questions
Select inputs because they target a requirement, a boundary, or a suspected defect.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
12
Type
Example
Expected check
Nominal
OR with known a and b
Exact result and error=0
Boundary
CTZ(0); shift by 0 or 31
Defined edge behavior
Negative control
MAX without SUB
error=1; capture zero
Timing / reset
valid_in=0; reset mid-traffic
Hold, clear, recover
Bug reproducer
MAX(10,20)
Detect the isolated defect
Small, intentional tests explain failures quickly.
Notes: Separate directed examples from exhaustive finite sweeps and random exploration. Explain why CTZ zero, high-half CPOP, and SEXT.B bit7 are powerful. Negative requests check error and data behavior. Hold checks must preserve previous result while error remains live. An isolated bug test makes debugging reproducible.
Evidence / source files:
tb/sequences; docs/02_test_plan/BMU_Test_Plan.md
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 13
03 / CHALLENGE THE DESIGN
Three kinds of random exploration
Each family generates 100 requests per run; the monitored reset adds one sample.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
13
Legal random
Valid operation + legal modifiers
Broad operand combinations
Seeds 101 / 102 / 103
Corner random
Independent corners for a and b
0, all ones, signed limits, patterns
Seeds 201 / 202 / 203
Error random
Ten invalid-request classes
Conflicts and missing requirements
Seeds 301 / 302 / 303
Directed tests target known risks. Random tests explore combinations. Seeds reproduce stimulus.
Notes: Legal random covers all 17 operation classes and allowed modifiers. Corner random independently picks a and b; pairing the same corner for both would miss important comparisons. Error random selects among ten invalid-request classes; the systematic guard matrix is broader. Seeds use Xcelium -svseed, and actual effective seeds are reported. Repeatability applies to stimulus under the same source/tool/configuration, not byte-identical timestamped logs.
Evidence / source files:
tb/sequences/base/random_legal_seq.sv; tb/sequences/base/random_corner_weighted_seq.sv; tb/sequences/error_injection/random_error_seq.sv; regression/configs/full.cfg
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 14
03 / CHALLENGE THE DESIGN
Assertions guard behavior across cycles
The scoreboard checks data. Assertions express signal-level and temporal rules.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
14
@(posedge clk) disable iff (!rst_l)
!valid_in |=> $stable(result_ff);
Reset
Clear result
Suppress error
Timing / hold
Hold when disabled
Known enabled result
Control guards
CSR conflict
Missing SUB / ZBA
Audience check: result holds, but error changes while valid_in=0. Is that allowed?
Notes: Explain the preponed sampling semantics before reading the implication. This exact property uses non-overlapped implication: a low valid sample requires stability at the next sampled edge, consistent with the enabled register. Reset disables this property. The timing sequence separately checks pre-edge behavior. There are 13 properties, including required-control and live-error checks.
Evidence / source files:
tb/assertions/bmu_protocol_assertions.sv; tb/sequences/reset_ops/latency_check_seq.sv
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 15
04 / MEASURE AND DEBUG
Coverage measures exercise, not correctness
Different coverage types answer different questions.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
15
Functional coverage
Did we exercise the planned scenarios?
Operations, modes, count values, crosses
Code coverage
Which RTL structures were exercised?
Blocks, scored expressions, toggles
Assertion coverage
Which properties were exercised?
Read coverage separately from failures
Can functional coverage be 100% while the DUT is wrong? Yes—this project demonstrates it.
Notes: Answer the previous question: yes, error is live even while result is held. Functional coverage measures specified scenarios, crosses, and boundaries. Code coverage measures instrumented structures, not requirement correctness. Assertion coverage is distinct from assertion pass/fail. Some covered properties also fail. There is no FSM report. Ask whether 100% functional coverage can coexist with failing tests; answer yes, demonstrated by this project.
Evidence / source files:
docs/07_coverage_reports/final_coverage_summary.md; tb/env/coverage/bmu_coverage.sv
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 16
04 / ADVANCED VERIFICATION
Beyond smoke tests: systematic stress
Finite sweeps complement random testing and make coverage closure deliberate.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
16
Control mutation matrix
Legal base → add forbidden field
Also remove required SUB / ZBA
Boundary enumeration
32 shift/index values; counts 0–32
256 bytes; 32 GREV encodings
Race-aware checking
Falling-edge drive, post-update sample
Reset/hold state in the predictor
Reproducible evidence
Effective seeds, isolated logs
Source and log SHA-256 fingerprints
Coverage closure uses 5,036 comparisons on the original DUT; failures remain visible.
Notes: The guard matrix mutates forbidden fields one at a time from legal requests, with both valid states, CSR conflicts, and required-modifier removal. SUB plus SLT/MAX can be a legal transition, not automatically a conflict. Closure sweeps all indices and count values. SEXT.B uses all 256 low bytes with upper-bit variation. Coverage exclusions represent impossible classification crosses rather than waived DUT failures. Provenance includes input and log SHA-256 hashes.
Evidence / source files:
tb/sequences/smoke/bmu_guard_matrix_seq.sv; tb/sequences/smoke/bmu_coverage_closure_seq.sv; results/reports/run_manifest.json
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 17
04 / RESULTS
Measured results: exercise achieved, bugs remain
Recorded baseline: 22 September 2026 • original DUT • coverage test seed 4
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
17
26
runs: 3 pass / 23 fail
562 / 562
functional bins hit
9
open DUT findings
Functional
100.00%
DUT blocks
16 / 16
DUT toggles
1,230 / 1,892
3/3 scored expressions only. Toggle coverage is incomplete. No DUT correctness sign-off.
Notes: 26 full-regression runs: 3 passing tests are model self-test, OR smoke, timing/reset. The other 23 fail, with zero UVM fatals. Coverage run has 5036 comparisons: 3488 match and 1548 mismatch; 513 native assertion failure messages. Code coverage is cumulative within bmu_tb_top.dut. Expression coverage is only three scored items, not complete condition coverage. Assertion coverage 11/13 is not a pass rate.
Evidence / source files:
results/reports/regression_summary.csv; results/reports/dut_coverage.txt; results/reports/assertion_coverage.txt; docs/07_coverage_reports/final_coverage_summary.md
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 18
04 / BUG REVIEW
Nine findings, four recurring defect patterns
All open; one critical and eight major. Each has a seed-1 isolated reproducer.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
18
Count / bit ordering
001: CPOP ignores upper half
009: CTZ reversal ordering
Data arrangement
002: PACK halves reversed
005: GREV swaps halfwords
Source selection
003: CSR sources reversed
010: MAX chooses wrong operand
Missing rejection
006: incomplete guards
007: missing SUB; 008: invalid GREV
BUG-008 depends on CLARIF-004. BUG-004 was withdrawn; pure CSR bypass is legal.
Notes: CPOP FFFF0000 should return 16, but returns 0 because the implementation counts only low 16 bits. Group findings to explain design failure patterns. BUG006 is critical; the others are major. BUG008 is confirmed against the adopted GREV invalid-encoding assumption. BUG004 was withdrawn and its ID is not reused. Appendix gives exact examples.
Evidence / source files:
docs/04_bug_reports/BMU_Bug_Log.md; results/bugs
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 19
04 / DEBUG ONE DEFECT
MAX root cause: the selector is inverted
The isolated request removes unrelated controls and makes the cause visible.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
19
bitmanip_minmax_sel_a = ge ^ ap_max; // original RTL
Compare
10 >= 20
ge = 0
Select
0 XOR 1
select_a = 1
Observe
a is selected
result = 10
Reproduce → isolate → inspect cause → propose correction → rerun related tests.
Notes: Actual original RTL assigns bitmanip_minmax_sel_a = ge ^ ap_max. For a=10, b=20: ge=0, ap_max=1, so selector is 1 and chooses a. That is 10 rather than 20. The corrected variant expresses the signed comparison directly. Do not confuse a minimal suspected edit with validated closure of all signed comparisons.
Evidence / source files:
rtl/Bit_Manipulation_Unit.sv:396; results/bugs/BMU-BUG-010.txt; docs/04_bug_reports/BMU_Bug_Log.md
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 20
05 / CORRECT AND CLOSE
What the exploratory RTL correction changes
The repository contains fix_v1 code. It is separate from the measured submission DUT.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
20
// MAX: select using a signed comparison
corrected_result = ($signed(a_in) > $signed(b_in)) ? a_in : b_in;
Path
Correction present in fix_v1
CPOP / CTZ
Count all 32 bits; scan CTZ from bit 0, default 32
PACK / GREV
Restore halfword order / reverse all four bytes
CSR write
csr_imm ? b_in : a_in
Control checks
Separate guard logic and required-control checks
Code changes exist; corrected-DUT regression closure is not established by this evidence.
Notes: These expressions are from the existing exploratory fixed variant. MAX uses an explicit signed comparison, CPOP iterates all 32 bits, PACK and GREV are reassembled correctly, CSR data selection is restored, CTZ scans from low bit with default 32. The fixed variant also has its own guard implementation. Do not claim this variant meets all legal masks or passes current regression: the submitted baseline does not establish that.
Evidence / source files:
rtl/Bit_Manipulation_Unit_fix_v1.sv:175–227; sim/filelists/xcelium_fix.f; tb/top/bmu_tb_top_fix_v1.sv
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 21
05 / CORRECT AND CLOSE
When can we honestly call a bug fixed?
A code edit is the start of closure, not the end.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
21
1 Reproduce
Original DUT fails
Same test and seed
2 Retest
Corrected DUT passes
Same expected result
3 Expand
Related boundaries
Full regression
4 Record
Source + seed + logs
Update bug disposition
Current status: nine original-DUT bugs open; fix_v1 remains exploratory.
Notes: Explain a counterfactual original-vs-fixed comparison. Keep the original failing test and run the same stimulus on the corrected DUT. Add related signed boundaries, equality, reversed operands and invalid MAX controls. Regress all scoped behavior and investigate any remaining/new failures. Update the bug only with exact source, tool, seed, and evidence. Current project leaves nine original-DUT findings open.
Evidence / source files:
docs/04_bug_reports/BMU_Bug_Log.md; docs/08_signoff/BMU_Signoff_Report.md
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 22
05 / FINAL ASSESSMENT
What this verification established
A traceable path from requirements to reproducible evidence.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
22
Established
17 operation classes exercised
865 predictor self-checks passed
562 functional bins exercised
Nine reproducible DUT findings
Still open
Original RTL defects
Corrected-DUT validation
Incomplete toggle coverage
Three documented assumptions
The deliverable is reproducible verification evidence, with clear limits and open findings.
Notes: Conclude with the real achievement: an executable verification method and nine isolated findings. Functional coverage closure applies to defined bins only. Remaining risks: timing/scan, unsupported GREV encoding, pure CSR interpretation, incomplete toggle coverage, excluded operations, and no validated fixed-DUT baseline. Invite questions; click a reference card to jump into the appendix.
Evidence / source files:
docs/08_signoff/BMU_Signoff_Report.md; docs/03_clarifications_log/spec_clarifications_log.md
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 23
APPENDIX / A
Operation reference
32-bit results; shift/index uses b[4:0]; arithmetic wraps modulo 2³².
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
23
Family
Expected behavior / legal mode
OR / XOR
Normal b, or inverted b with zbb=1
SRL / SRA / ROR / BINV
Logical / arithmetic / rotate / invert indexed bit
SH2ADD / SUB
(a<<2)+b with ZBA; a-b without ZBA
SLT / MAX
Require SUB; SLT allows unsigned; MAX is signed
CTZ / CPOP / SEXT.B
Trailing zeros (zero→32); set bits; sign-extend bit 7
PACK / GREV
{b[15:0],a[15:0]}; byte reverse for b[4:0]=24
CSR read / write
Pure bypass; write selects b if immediate else a
Notes: Use this slide as a quick reference, not a slide to read aloud. SLT signedness is a mode within one operation class. The project excludes standalone unspecified operation behavior while testing those control bits as forbidden companions.
Evidence / source files:
README.md §2; docs/00_spec/BMU_Specification_v1.2.pdf
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 24
APPENDIX / B
Bug evidence: data-path defects
All examples reproduced on the original DUT, seed 1. Hex values have a 0x prefix.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
24
Bug
Stimulus
Expected → observed
001 CPOP
a=0xFFFF0000
16 → 0
002 PACK
a=0x1234, b=0x5678
0x56781234 → 0x12345678
003 CSR
a=0x33334444, b=0x11112222
Immediate and register sources reversed
005 GREV
a=0x12345678, b=24
0x78563412 → 0x56781234
009 CTZ
a=1
0 → 1
010 MAX
a=10, b=20; max+sub
20 → 10
Notes: BUG003 has both mode directions in the evidence. BUG005 is the valid encoding and is distinct from invalid GREV guard BUG008. Each file results/bugs/BMU-BUG-NNN.txt includes command, source log hash, exact mismatch and UVM totals.
Evidence / source files:
results/bugs/BMU-BUG-001.txt; results/bugs/BMU-BUG-002.txt; results/bugs/BMU-BUG-003.txt; results/bugs/BMU-BUG-005.txt; results/bugs/BMU-BUG-009.txt; results/bugs/BMU-BUG-010.txt
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 25
APPENDIX / C
Bug evidence: control guards and assumptions
Invalid captured requests require zero result and error=1 under the adopted rules.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
25
Bug
Invalid request
Failure
006 • Critical
Empty ap; no CSR read
error=0 instead of 1
007 • Major
SLT or MAX without SUB
error=0; MAX may return nonzero data
008 • Major
GREV with b[4:0]=5
error=0 under CLARIF-004
Recorded assumptions
001: timing/reset/scan • 004: invalid GREV • 005: pure CSR read versus conflict
Notes: BUG006 empty control example result remains zero but error is incorrectly zero; broad matrix finds additional missing guard paths. BUG007 SLT without SUB uses a=FFFFFFFF,b=1; MAX without SUB uses 10,20 and returns20 with no error. BUG008 uses b=5 and expected invalid rejection per CLARIF004. Three assumption-tagged items are not design-team confirmations.
Evidence / source files:
results/bugs/BMU-BUG-006.txt; results/bugs/BMU-BUG-007.txt; results/bugs/BMU-BUG-008.txt; docs/03_clarifications_log/spec_clarifications_log.md
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 26
APPENDIX / D
Assertion and coverage reference
Use properties, functional bins, and code metrics together.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
26
reset_suppresses_error
reset_clears_result
result_holds_when_invalid
valid_result_is_registered
one_primary_operation
empty_valid_request
live_error_when_invalid
csr_conflict
sh2add_requires_zba
sub_rejects_zba
slt_requires_sub
max_requires_sub
grev_encoding
Functional dimensions
Operations × patterns; valid/error
Shift/index; CTZ/CPOP count; modes
Measurement limits
11/13 assertion coverage ≠ pass rate
3 scored expressions ≠ every expression
65.01% toggles; no FSM claim
Notes: List all 13 actual property names for technical questions. valid_result_is_registered checks a known result, not complete capture timing; directed timing tests cover the latter. Coverage cross exclusions remove impossible classification pairs, not DUT failures. No code refinement exclusions or complete reachability proof were applied.
Evidence / source files:
tb/assertions/bmu_protocol_assertions.sv; tb/env/coverage/bmu_coverage.sv; docs/07_coverage_reports/coverage_waivers.md
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 27
APPENDIX / E
Reproduce the evidence
Run from the repository root with Xcelium and a working Cadence license.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
27
# Passing setup checks
make -C sim run TEST=bmu_model_self_test SEED=1
make -C sim run TEST=bmu_timing_reset_test SEED=1
# Full regression and isolated MAX failure
make -C sim regression
make -C sim run TEST=bmu_bug_010_test SEED=1
# Coverage extraction after the coverage test
imc -exec sim/scripts/report_coverage.tcl
Expected DUT failures remain failures. Zero UVM fatals does not mean every test passed.
Notes: The full regression and isolated bug tests return nonzero on the original DUT. Run IMC separately after simulation, not chained with &&. The IMC script loads the seed4 coverage database. Focused regression rewrites local summary/manifest; preserve baseline evidence before recording new measurements. Makefile supports Xcelium; VCS/Questa are not supported.
Evidence / source files:
sim/Makefile; sim/scripts/report_coverage.tcl; regression/configs/full.cfg; README.md §10
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.

## Slide 28
APPENDIX / F
Where to find the supporting evidence
The README is the project walkthrough; these files hold the detailed records.
BMU VERIFICATION / JHT127 / ORIGINAL-DUT BASELINE: 22 SEP 2026
MENU
28
Question
Repository artifact
What was required?
docs/00_spec/BMU_Specification_v1.2.pdf
What was tested?
docs/02_test_plan/BMU_Test_Plan.md
What failed?
docs/04_bug_reports/BMU_Bug_Log.md + results/bugs/
What ran?
results/reports/regression_summary.csv
What produced the results?
results/reports/run_manifest.json
What are the limits?
docs/08_signoff/BMU_Signoff_Report.md
Questions? Return to MENU to revisit any part of the verification story.
Notes: Direct the audience to the retained compact evidence rather than untracked generated databases. Raw logs, coverage DB and waveforms are regenerated locally. The run manifest records hashes of measured verification sources and logs. The README and presentation can evolve without implying that the simulation baseline was rerun.
Evidence / source files:
README.md; docs/README.md; results/reports/run_manifest.json
Presentation note: slides 1–22 form the main talk. Slides 23–28 are reference material. Use MENU to return to the clickable agenda. All measurements describe the original DUT unless explicitly labelled exploratory.