## Slide 1
VERIFICATION PROJECT | BMU
RISC-V BMU
Design Verification Project
Scope
Spec-driven verification
Bug tracking & evidence
Method
Assertions + coverage
Independent reference model
Main message
Not just tests — a credible verification package.
Actual project facts
8 open bug IDs
1 passed / 2 failed regression
100% closure coverage

## Slide 2
What I accomplished
The project is not only about RTL; it is about verification discipline
01
Built a UVM verification environment in tb/ for the BMU DUT.
Created directed and random tests for valid, invalid, corner, and guard cases.
Added protocol assertions to check reset, validity, and illegal-control behavior.
Captured real bug evidence in the bug register and kept the original DUT untouched.
Kept the repo clean, structured, and traceable for a professional review.
Why it matters
Evidence-based stance

## Slide 3
Verification architecture
Spec-driven flow with independent reference checking
02
Spec & clarification log
UVM testbench
Reference model
Scoreboard + assertions
Why this is strong
Outcome

## Slide 4
Tests that actually exist
Real verification runs, not placeholders
03
bmu_gap_checks_test: targeted bug reproduction and mismatch capture.
bmu_nominal_directed_test: valid-operation nominal validation.
bmu_error_directed_test: invalid-control and guard checks.
bmu_legal_random_test and bmu_error_random_test: broad random legal/illegal sweeps.
bmu_coverage_closure_test: coverage-focused closure run with seed 4.
Test philosophy
Result

## Slide 5
Assertions and CI quality
I improved the verification quality and repo discipline
04
Assertions checked reset behavior, valid gating, GREV invalid encoding, and SUB co-requisites.
The bug register documents issues such as invalid guard acceptance and CTZ mismatch.
The CI docs check ran locally and returned: Documentation checks passed.
The guard also rejects unapproved RTL drift under rtl/ beyond the approved list.
CI evidence
Documentation checks passed
No unapproved RTL drift
Why it matters

## Slide 6
Key defects I found
These are real, traceable, and left Open
05
BMU-BUG-006
This is a critical guard issue.
BMU-BUG-007
The DUT did not enforce it.
BMU-BUG-009
BMU-BUG-001
Status

## Slide 7
Measured results
These numbers come from the project logs and coverage reports
06
Regression
2 failed
from the directed regression run
Gap check
63.32% functional coverage
Closure run
100.00% functional coverage
seed 4
Professional interpretation

## Slide 8
Repo structure and project polish
The work is organized for review, not just for code storage
07
rtl/ contains the original RTL plus clearly isolated fix-version artifacts.
tb/ contains the UVM environment, interface, packages, assertions, and tests.
docs/ holds the spec, verification plan, bug register, coverage, signoff, and presentation files.
results/ stores simulator logs, coverage results, and bug evidence.
The repo is structured to make the story easy to defend during review or presentation.
Extra effort

## Slide 9
Final takeaway
This is a complete verification story, not just a code assignment
08
I traced the DUT against the specification and the clarification log.
I built the testbench, assertions, coverage flow, and evidence package.
I captured the defects honestly and kept the original RTL separate from the fix investigation.
That is exactly the kind of engineering narrative professors want to hear: evidence, structure, and honesty.
Presenter note

## Slide 10
Thank you
Questions?
This project shows a real verification workflow: spec -> test -> compare -> evidence -> documented defects.