## Slide 1
BMU VERIFICATION PROJECT
From specification to bug evidence
01
A 32-bit BMU.
A complete verification story.
SystemVerilog + UVM
Directed + random testing
Assertions + coverage
17
operation classes
562
functional bins hit
9
open DUT findings
Original RTL. Reproducible failures.
Trace one MAX request to the defect.
01

## Slide 2
INTERACTIVE AGENDA
The verification route
Specification → stimulus → evidence
02
01 Understand
Specification, controls, timing, DUT
02 Follow a request
Environment and MAX transaction
03 Test the design
Directed, random, assertions
04 Measure + debug
Coverage, results, nine findings
05 Correct + close
Existing fix code and validation gate
06 Explore details
Operations, evidence, commands
Audience checkpoints: predict a result • classify a failure • read assertions, coverage, and bug evidence.
02

## Slide 3
01 / UNDERSTAND
What does this BMU do?
32-bit operands in; a registered result and a live error out.
03
Logic and shift
OR, XOR, SRL, SRA, ROR, BINV
Arithmetic and compare
SH2ADD, SUB, SLT/SLTU, signed MAX
Count and rearrange
CTZ, CPOP, SEXT.B, PACK, GREV
CSR data paths
Bypass read and write-data selection
Predict: CPOP(0xFFFF0000) = ? Keep your answer for the bug review.
03

## Slide 4
01 / UNDERSTAND
Turn the specification into checks
Example requirement: signed MAX selects the larger operand and requires SUB.
04
REQUIREMENT
Signed MAX
max=1, sub=1
STIMULUS
a=10, b=20
valid_in=1
ORACLE
result=20
error=0
EVIDENCE
Compare + log
cover scenario
Negative companion test
Remove SUB: require error=1 and captured result=0.
Record ambiguities
Timing, GREV invalid encoding, CSR conflicts.
One selected operation can require several control bits. “Legal” is not simply one-hot.
04

## Slide 5
01 / UNDERSTAND
The interface contract determines sampling
No ready signal. No output-valid handshake. valid_in enables result capture.
05
Inputs
a_in, b_in: 32 bits
ap: 42 control bits
CSR enable + read data
rst_l, valid_in, scan_mode
Falling edge
Driver applies request
Between edges
Combinational paths settle
Rising edge
Capture result; monitor samples
valid_in=0 → result holds. Invalid controls can still assert the live error output.
05

## Slide 6
01 / UNDERSTAND
Inside the DUT
Parallel datapaths feed a combined result; implemented error logic gates capture data.
06
Inputs
a, b, ap
CSR signals
Logic / CSR read
Adder / compare
Shift / rotate
Count / pack / bits
Combine
Masked OR
error → zero
Result register
result_ff[31:0]
reset / enable / hold
Live error: implemented guards are incomplete
Data bugs and missing control guards need different checks.
06

## Slide 7
02 / FOLLOW A REQUEST
The UVM environment: from sequence item to verdict
Stimulus in. Evidence out.
07
Sequence
Sequencer
Driver
Interface
DUT
Monitor
Reference model
Scoreboard + checker
expected
actual
Coverage
Scenarios exercised
Assertions
DUT outputs to interface
Active agent:
sequencer, driver, monitor
Predict from observed inputs. Compare result_ff and error under a fully independent reference model.
07

## Slide 8
02 / FOLLOW A REQUEST • STEP 1
Your turn: construct a legal MAX request
Predict first.
08
// Transaction values
rst_l = 1;
valid_in = 1;
ap.max = 1;
ap.sub = 1;
a_in = 10;
b_in = 20;
Question 1
Is max=1 alone a legal request?
Question 2
What should result_ff and error be for a legal signed MAX request?
Next: drive → sample → compare
08

## Slide 9
02 / FOLLOW A REQUEST • STEP 2
The request becomes pin-level activity
Sequence item → sequencer → driver → interface → DUT → monitor → predictor → scoreboard
09
// UVM handshake — simplified
start_item(req);
// fill request fields
finish_item(req);
// Driver: get → drive → item_done
10 ns: falling edge
Drive legal request: max=1, sub=1, a=10, b=20
15 ns: rising edge
Monitor captures result_ff and compares with the expected result
Drive MAX, SUB, a=10, b=20
10–15 ns: compute
Result path and live error settle
15 ns: rising edge
Register updates; monitor samples
Driven ≠ correct.
Expected: result_ff=20, error=0
09

## Slide 10
02 / FOLLOW A REQUEST • STEP 3
The scoreboard exposes the MAX defect
Same observed request. Independent prediction. Different data.
10
EXPECTED
result_ff = 20
error = 0
ACTUAL
result_ff = 10
error = 0
VERDICT
Mismatch
BMU-BUG-010
@ 15 ns expected: 0x00000014 / error=0 actual: 0x0000000a / error=0
A scenario can be covered and incorrect at the same time.
10

## Slide 11
02 / TRUST THE ENVIRONMENT
Who is checking the checker?
A useful failure must distinguish a DUT defect from a testbench issue using independent prediction, assertions, and a clean signal contract.
11
865 predictor self-checks
Legal, invalid, boundary and state cases
Passing setup checks
OR smoke and timing/reset tests
Complete comparisons
Result + error; four-state equality; queue checks
Honest failure detection
UVM errors, assertions and incomplete runs fail
Prediction is independent of RTL. Coverage shares specification classification helpers.
11

## Slide 12
03 / CHALLENGE THE DESIGN
Directed testing asks precise questions
Select inputs because they target a requirement, a boundary, or a suspected defect.
12
Type
Example
Expected check
Nominal
OR with known a and b
Exact result and error=0
Boundary
CTZ(0); shift by 0 or 31
Defined edge behavior
Negative control
MAX without SUB
error=1; capture zero
Timing / reset
valid_in=0; reset mid-traffic
Hold, clear, recover
Bug reproducer
MAX(10,20)
Detect the isolated defect
Small, intentional tests explain failures quickly.
12

## Slide 13
03 / CHALLENGE THE DESIGN
Three kinds of random exploration
Each family generates 100 requests per run; the monitored reset adds one sample.
13
Legal random
Valid operation + legal modifiers
Broad operand combinations
Seeds 101 / 102 / 103
Corner random
Independent corners for a and b
0, all ones, signed limits, patterns
Seeds 201 / 202 / 203
Error random
Ten invalid-request classes
Conflicts and missing requirements
Seeds 301 / 302 / 303
Directed tests target known risks. Random tests explore combinations. Seeds reproduce stimulus.
13

## Slide 14
03 / CHALLENGE THE DESIGN
Assertions guard protocol behavior across cycles
Scoreboard: data. Assertions: time and protocol.
14
@(posedge clk) disable iff (!rst_l)
!valid_in |=> $stable(result_ff);
Reset
Clear result
Suppress error
Timing / hold
Hold when disabled
Known enabled result
Control guards
CSR conflict
Missing SUB / ZBA
Audience check: result holds, but error changes while valid_in=0. Is that allowed?
14

## Slide 15
04 / MEASURE AND DEBUG
Coverage measures exercise; assertions + independent prediction confirm correctness and make the flow CI-ready
Three lenses. One verdict.
15
Functional coverage
Did we exercise the planned scenarios?
Operations, modes, count values, crosses
Code coverage
Which RTL structures were exercised?
Blocks, scored expressions, toggles
Assertion coverage
Which properties were exercised?
Read coverage separately from failures
100% bins ≠ correctness
15

## Slide 16
04 / ADVANCED VERIFICATION
Beyond smoke tests: systematic stress
Sweeps + random + assertions = repeatable closure.
16
Control mutation matrix
Legal base → add forbidden field
Also remove required SUB / ZBA
Boundary enumeration
32 shift/index values; counts 0–32
256 bytes; 32 GREV encodings
Race-aware checking
Falling-edge drive, post-update sample
Reset/hold state in the predictor
Reproducible evidence
Effective seeds, isolated logs
Source and log SHA-256 fingerprints
Coverage closure uses 5,036 comparisons on the original DUT; failures remain visible.
16

## Slide 17
04 / RESULTS
Measured results: exercise achieved, bugs remain
Recorded baseline: 22 September 2026 • original DUT • coverage test seed 4
17
26
runs: 3 pass / 23 fail
562 / 562
functional bins hit
9
open DUT findings
Functional
100.00%
DUT blocks
16 / 16
DUT toggles
1,230 / 1,892
3/3 scored expressions only. Toggle coverage is incomplete. No DUT correctness sign-off.
17

## Slide 18
04 / BUG REVIEW
Nine findings, four recurring defect patterns
All open; one critical and eight major. Each has a seed-1 isolated reproducer.
18
Count / bit ordering
001: CPOP ignores upper half
009: CTZ reversal ordering
Data arrangement
002: PACK halves reversed
005: GREV swaps halfwords
Source selection
003: CSR sources reversed
010: MAX chooses wrong operand
Missing rejection
006: incomplete guards
007: missing SUB; 008: invalid GREV
BUG-008 depends on CLARIF-004. BUG-004 was withdrawn; pure CSR bypass is legal.
18

## Slide 19
04 / DEBUG ONE DEFECT
MAX root cause: the selector is inverted
The isolated request removes unrelated controls and makes the cause visible.
19
bitmanip_minmax_sel_a = ge ^ ap_max; // original RTL
Compare
10 >= 20
ge = 0
Select
0 XOR 1
select_a = 1
Observe
a is selected
result = 10
Reproduce → isolate → inspect cause → propose correction → rerun related tests.
19

## Slide 20
05 / CORRECT AND CLOSE
What the exploratory RTL correction changes
The repository contains exploratory fix_v1 code. It is deliberately separated from the measured submission-DUT baseline.
20
// MAX: select using a signed comparison
corrected_result = ($signed(a_in) > $signed(b_in)) ? a_in : b_in;
Path
Correction present in fix_v1
CPOP / CTZ
Count all 32 bits; scan CTZ from bit 0, default 32
PACK / GREV
Restore halfword order / reverse all four bytes
CSR write
csr_imm ? b_in : a_in
Control checks
Separate guard logic and required-control checks
Code changes exist; corrected-DUT regression closure is not established by this evidence.
20

## Slide 21
05 / CORRECT AND CLOSE
When can we honestly call a bug fixed with evidence?
A code edit is the start of closure, not the end.
21
1 Reproduce
Original DUT fails
Same test and seed
2 Retest
Corrected DUT passes
Same expected result
3 Expand
Related boundaries
Full regression
4 Record
Source + seed + logs
Update bug disposition
Current status: nine original-DUT bugs open; fix_v1 remains exploratory.
21

## Slide 22
05 / FINAL ASSESSMENT
What this project demonstrates: advanced verification capability
Specification → evidence → closure
22
Established
17 operation classes exercised
865 predictor self-checks passed
562 functional bins exercised
Nine reproducible DUT findings
Still open
Original RTL defects
Corrected-DUT validation
Incomplete toggle coverage
Three documented assumptions
Evidence with limits.
22

## Slide 23
APPENDIX / A
Operation reference
32-bit results; shift/index uses b[4:0]; arithmetic wraps modulo 2³².
23
Family
Expected behavior / legal mode
OR / XOR
Normal b, or inverted b with zbb=1
SRL / SRA / ROR / BINV
Logical / arithmetic / rotate / invert indexed bit
SH2ADD / SUB
(a<<2)+b with ZBA; a-b without ZBA
SLT / MAX
Require SUB; SLT allows unsigned; MAX is signed
CTZ / CPOP / SEXT.B
Trailing zeros (zero→32); set bits; sign-extend bit 7
PACK / GREV
{b[15:0],a[15:0]}; byte reverse for b[4:0]=24
CSR read / write
Pure bypass; write selects b if immediate else a
23

## Slide 24
APPENDIX / B
Bug evidence: data-path defects
All examples reproduced on the original DUT, seed 1. Hex values have a 0x prefix.
24
Bug
Stimulus
Expected → observed
001 CPOP
a=0xFFFF0000
16 → 0
002 PACK
a=0x1234, b=0x5678
0x56781234 → 0x12345678
003 CSR
a=0x33334444, b=0x11112222
Immediate and register sources reversed
005 GREV
a=0x12345678, b=24
0x78563412 → 0x56781234
009 CTZ
a=1
0 → 1
010 MAX
a=10, b=20; max+sub
20 → 10
24

## Slide 25
APPENDIX / C
Bug evidence: control guards and assumptions
Invalid captured requests require zero result and error=1 under the adopted rules.
25
Bug
Invalid request
Failure
006 • Critical
Empty ap; no CSR read
error=0 instead of 1
007 • Major
SLT or MAX without SUB
error=0; MAX may return nonzero data
008 • Major
GREV with b[4:0]=5
error=0 under CLARIF-004
Recorded assumptions
001: timing/reset/scan • 004: invalid GREV • 005: pure CSR read versus conflict
25

## Slide 26
APPENDIX / D
Assertion and coverage reference
Use properties, functional bins, and code metrics together to build a verification stack that is both rigorous and CI-friendly.
26
reset_suppresses_error
reset_clears_result
result_holds_when_invalid
valid_result_is_registered
one_primary_operation
empty_valid_request
live_error_when_invalid
csr_conflict
sh2add_requires_zba
sub_rejects_zba
slt_requires_sub
max_requires_sub
grev_encoding
Functional dimensions
Operations × patterns; valid/error
Shift/index; CTZ/CPOP count; modes
Measurement limits
11/13 assertion coverage ≠ pass rate
3 scored expressions ≠ every expression
65.01% toggles; no FSM claim
26

## Slide 27
APPENDIX / E
Reproduce the evidence
Run from the repository root with Xcelium and a working Cadence license.
27
# Passing setup checks
make -C sim run TEST=bmu_model_self_test SEED=1
make -C sim run TEST=bmu_timing_reset_test SEED=1
# Full regression and isolated MAX failure
make -C sim regression
make -C sim run TEST=bmu_bug_010_test SEED=1
# Coverage extraction after the coverage test
imc -exec sim/scripts/report_coverage.tcl
Expected DUT failures remain failures. Zero UVM fatals does not mean every test passed.
27

## Slide 28
APPENDIX / F
Where to find the supporting evidence
The README is the project walkthrough; these files hold the detailed records.
28
Question
Repository artifact
What was required?
docs/00_spec/BMU_Specification_v1.2.pdf
What was tested?
docs/02_test_plan/BMU_Test_Plan.md
What failed?
docs/04_bug_reports/BMU_Bug_Log.md + results/bugs/
What ran?
results/reports/regression_summary.csv
What produced the results?
results/reports/run_manifest.json
What are the limits?
docs/08_signoff/BMU_Signoff_Report.md
Evidence map
28